## Slide 1: DAE-Aware Bayesian Inference for Joint Generator-Network Parameter Estimation
Abdallah Alalem Albustami, Ahmad F. Taha, and Sankaran Mahadevan

## Slide 2: Motivation
Estimating generator parameters (inertia, damping)
Estimating network parameters (susceptance, conductance)
Inertia
Damping
Conductance
Susceptance
Parameters change (rewinding, aging, temp.), need accurate estimates
Decoupled
Notes: Algebraic constraints (power flow equations or the current admittance form)

## Slide 3: Motivation
Inertia
Damping
Conductance
Susceptance
Coupled
Nonlinear Differential Algebraic Equations Model (DAE)
Generator dynamics (2nd to 8th order)
Algebraic constraints
Notes: Algebraic constraints (power flow equations or the current admittance form)

## Slide 4: Not another estimator
Does uncertainty in network or generator parameters bias the estimation of the other parameter group?

## Slide 5: Literature
EKF, UKF, CKF
LS, TLS, WLS
Want an uncertainty-aware approach for the coupled generator-network DAE inverse problem
Point estimates, decouple the estimation problem
DREM
Observers
Bayesian Inference
Optimization
ML methods

## Slide 6: Problem
Given
while enforcing DAE consistency
Obtain
Parameter estimates
Quantify uncertainty
Understand the coupling
Measurements (PMU data)
Prior knowledge of parameters
realistic

## Slide 7: Outline
Power System DAE Model
Measurement Model
Sensitivity & Identifiability
Bayesian Inference
DAE MCMC
Case Studies
Limitations &
Conclusion

## Slide 8: Physics DAE to Sensitivity ODE
DAE model
Bus voltage phasors
Frequency deviations
Measurement Model
Measurement Sensitivity
Sensitivity Matrices
Variational System
Sensitivity ODE
Schur-complement elimination

## Slide 9: Co-Identifiability
Measurement Sensitivity
Log-Normal Reparameterization
Enforce positivity
Models uncertainty as deviations from nominal values
Gauss-Newton curvature matrix
How strongly PMU residuals change when parameters are perturbed
Co-identifiability index
How strongly two parameter groups are co-identified from same data
Notes: (H) tells us how strongly the data push back when we perturb the parameters. If changing a parameter produces a large change in the residuals, then the corresponding curvature is large, and that parameter is locally easier to identify.
Finally, we use this matrix to define a co-identifiability index between parameter groups. The idea is to look at the off-diagonal block of (H) that couples two groups, and normalize it by the strength of the two diagonal blocks.

## Slide 10: Bayesian Inference
posterior
likelihood
marginal likelihood (normalization)
parameters
measurements
Posterior = Likelihood x Prior ÷ Evidence
prior

## Slide 11: Likelihood
Probability of observing data under hypothetical parameter values
No. of samples
Take the log of the multivariate Gaussian density of independent samples over time
Penalizes residuals, weighted by uncertainty
Measurement noise and model discrepancy covariance
Residuals

## Slide 12: Likelihood: Time Segmentation
Electromechanical transients exhibit useful time-scale separation:
  Initial freq. swing: inertia
  Oscillation decay: damping
  Settling response: admittance
Introduce channel specific weights to emphasize informative channels

## Slide 13: Priors
Series r and x are positive, subject to multiplicative uncertainty (aging, temperature), we use log-normal priors
We sample (r, x) then assemble Ybus
M and D are positive, subject to multiplicative uncertainty (aging, rewinding), we use log-normal priors
centered at nominal values (not true values)
Assumed independent across generators before PMU data update them
Generator Parameters
Network Parameters

## Slide 14: Priors
The full prior combines generator priors, network priors, and a final power flow feasibility check

## Slide 15: Posteriors
Target posterior: data fit, physics feasibility, and prior information
No normalization needed: MCMC compares ratios
Log posterior looks like this
Data moves posterior towards true when DAE response improves

## Slide 16: MCMC
MCMC: Sampling method that explores posterior by repeatedly proposing parameter values, keeping the ones that explain the data well, and using the accepted samples to estimate uncertainty.

## Slide 17: DAE MCMC
Perturb one block
Obtain
Physical parameters
check box constraints
Full DAE Solve
Metropolis correction
Accept with probability
Coarse DAE Filter
Filter bad proposals
Accept with probability
Initialize
Nonlinear LS
Current MCMC state
Target posterior
Exact DAE-aware
PF Filter ( )
Infeasible  reject

## Slide 18: Practical DAE MCMC
Every posterior evaluation costs a power flow solve + a full DAE simulation Sampler must make each solve count:
Smart Start
Stagewise Initialization
Stage A: fit (M, D) to frequency channels
Stage B: fit (r, x) to all channels
Joint step refines both
Blocked Proposals
Gibbs + Adaptive Covariance
Cycle through (M, D), r, then x
Gaussian steps in standardized log-space
Delayed Acceptance
Multifidelity Filter
Stage 0: PF infeasible? reject
Stage 1: coarse DAE screens cheaply
Stage 2: full DAE for survivors
Outcome: same posterior as plain Metropolis-Hastings with fewer exact DAE solves.

## Slide 19: Case Studies
Simulate the DAE at perturbed true parameters, then add measurement noise
 | IEEE 9-bus | IEEE 39-bus
Role | Main validation | Larger proof-of-concept
System | 3 gen., 9 buses, 9 branches | 10 gen., 39 buses, 46 branches
Unknowns | nθ = 21 | nθ = 108
Measurements | 17 PMU channels | 68 PMU channels

## Slide 20: Co-Identifiability
Initial observation: weak co-identifiability. Oops, paper dead? Means sensitivity coupling is small at the chosen point (local)
Does not mean decoupled estimation is unbiased
Fixing an incorrect parameter group can still force the estimated group to compensate through the nonlinear DAE model

## Slide 21: Joint Estimation
Estimates move from nominal to real values
Uncertainty shrinks significantly from the prior
Generator and network parameters are calibrated together

## Slide 22: Joint vs. Decoupled
Joint closer to true values across all parameters
Decoupled shifts posterior because fixed parameter group is wrong
Bias seems largest for damping
Joint estimation gives tighter better-centered posteriors

## Slide 23: Computational Cost & Scaling
IEEE 9-bus: delayed acceptance reduces expensive full DAE solves
IEEE 39-bus
Proof-of-concept, under-calibrated
Run | Iterations | Time | Exact solves reduction | 95% CI coverage
Joint, reduced-budget | 500 | 7.2 min | 50.6% | 12/21
Joint, full-budget | 7000 | 30.4 min | 70.1% | 21/21
Metric | 39-bus results
Unknown parameters | 108
Run budget | 1000
Exact DAE solves | 765 (23.5% fewer)
Mean rel. error: M / D | 3.32% / 3.98%
Mean rel. error: r / x | 4.82% 2.45%
95% CI coverage | 14/108 (under calibrated)
Wall-clock time | 65.8 min
Reviewer 2 insisted

## Slide 24: Limitations
Scalability is hard but possible, suited for offline calibration
Needs informative data and recorded disturbance profiles
The inverse crime: data generated from the same model
Future work: real data, joint real-time calibration with UQ?

## Slide 25: Conclusion
Joint generator-network estimation matters, decoupled estimation can bias both sides
Framework provides uncertainty, credible intervals, and jointly consistent parameter sets
DAE-aware inference keeps parameter estimates tied to physical power flow feasibility

## Slide 26: Thank You Questions?

## Slide 27: MCMC: Blocked Gibbs Proposals
Split parameters into three blocks
Start from the full vector and draw a random Gaussian step for that block:
Proposal step
Then propose while keeping other blocks fixed
b: selected block db: number of parameters in the block sb: adaptive scalar step-size for block b
Lb: Cholesky factor of block covariance obtained from matrix H

## Slide 28: MCMC: Delayed Acceptance
Check whether proposal is acceptable:
Check box constraints , if not inside  reject
Map to physical parameters:
Solve PF with proposed parameter: if infeasible  reject
Run a coarse DAE simulation (relaxed tolerances), accept with probability (filter bad proposals to avoid full DAE solves)
Run full DAE simulation, accept with probability
If accepted:
: Cheap log-posterior (coarse)
: Exact log-posterior (full)

## Slide 29: MCMC: Stagewise initialization
For initialization, instead of starting MCMC from nominal values:
Use stagewise nonlinear least squares to start MCMC near a high-posterior region
Stage A estimates (𝑀, 𝐷) from frequency residuals with network fixed
Stage B estimates (𝑟, 𝑥) from all-channel residuals with dynamics fixed
Joint step: refine parameters, provide local curvature for proposal covariances